This page was exported from APEX DYNAMICS France [    http://www.apexdyna.fr    ]

Export date: Wed Apr 17 5:17:51 2024 / +0000 GMT

# SERIES AP

Product Categories: Réducteurs grande capacité de charge - Forte précision

Product Page: https://www.apexdyna.fr/produit/series-ap/

## Product Summary

Dédiés à des fonctionnements en régime permanent (S1) ou intermittent (S5)

- Couple nominal

T2N : 24 Nm - 5615 Nm (2 Etages)

- T2N : 1225 Nm - 10980 Nm (4 Etages)

Rapports de réduction

2-étages : 12 / 15 / 16 / 20 / 25 / 28 / 35 / 40 / 49 / 50 / 70 / 100

- 4-étages : 1225 / 1400 / 1750 / 2000 / 2800 / 3500 / 5000 / 7000 / 10 000

Jeu angulaire

2-étages : =2 arcmin (AHK064 = 3)

- 4-étages : =2 arcmin

Rendement

2-étages : 94%

- 4-étages : 90%

- Montage simplifié

Faible niveau de bruit

Tailles disponibles:

2 Etages: AHK064 / AHK090 / AHK110 / AHK140 / AHK200 / AHK255 / AHK285 / AHK355

- 4 Etages: AHK285 / AHK355 / AHK450

## Product Description

[vc_row][vc_column][vc_tabs][vc_tab title="SPÉCIFICATIONS" tab_id="1422960536-2-74"][vc_single_image image="1487" img_size="full"][vc_single_image image="1488" img_size="full"][vc_column_text]

# Inertie AP - APC

[/vc_column_text][vc_single_image image="1489" img_size="full"][vc_single_image image="1490" img_size="full"][/vc_tab][vc_tab title="DIMENSIONS" tab_id="1422960572297-2-2"][vc_single_image image="1484" img_size="full"][vc_single_image image="1483" img_size="full"][/vc_tab][vc_tab title="TÉLÉCHARGEMENTS" tab_id="1422960581994-3-0"][vc_column_text]Catalogue produits series AP

Catalogue général Apex Dynamics France

Certificat ATEX

Plans génériques[/vc_column_text][/vc_tab][/vc_tabs][/vc_column][/vc_row]

Product added date: 2020-10-20 12:26:01

Product modified date: 2020-10-20 16:18:13

Product export as MS Document by WooCommerce PDF & Print plugin.